## Slide 1
AS
Intelligent Scalable Multi-Agent Architecture for Product Development
Madhupranavi S
Revanth Kannan G
Siddhant Erande
A hierarchical, modular AI framework
spanning vehicle systems from concept to validation
Notes: 1.7.2013
1
‹#›

## Slide 2
The Problem We're Solving
Scope:
    Multi-domain Product Development — The framework spans all major engineering systems in a vehicle program — Integration, Vehicle System, CAB, E&E, Drivetrain, and Engine — each with their own subsystems and design complexity
    Subsystem-level intelligence — Within each domain, individual subsystems such as Frames, Suspension, Steering, and Fuel System are addressed independently with their own dedicated agent layer
    End-to-end engineering tasks — Each subsystem covers the full engineering workflow — from expert advisory and design calculations through to verification, validation, and failure mode analysis
Vision:
A connected, automated, intelligent layer across all PD systems
    Automated — Agents handle repetitive engineering tasks end-to-end
    Expert-Augmented — Domain knowledge and engineering rules embedded in every agent
    Connected — All systems communicate through a central orchestrator
Notes: 1.7.2013
2
‹#›

## Slide 3
ARCHITECTURE OVERVIEW
N · N-1 · N-2 · Agent Layer
N
Central
Orchestrator
N-1
Domain
Systems
N-2
Sub
Systems
Agents
Per Sub-
System
CENTRAL ORCHESTRATOR
Integration
Vehicle
System
CAB
E&E
Drivetrain
Engine
Frames
Suspension
Steering
Fuel
System
Others...
Same agent set for every subsystem — infinitely extensible
Expert
Advisor
Design
Calculation
Verification & Validation
DFMEA
+ More
Agents
Notes: 1.7.2013
2
‹#›

## Slide 4
WHY THIS APPROACH
    Modular — Each subsystem agent follows the exact same pattern. Once the framework is built for one subsystem like Suspension, the same blueprint applies directly to Steering, Frames, Fuel System, and every other subsystem without redesigning or rebuilding from scratch. This means parallel development across teams is possible from day one.
    Scalable — The N → N-1 → N-2 hierarchy is designed to grow. New domains, new subsystems, and new agent types can be plugged in at any level without touching the rest of the architecture. As the program expands, the system expands with it — not against it.
    Human-in-the-Loop — This is augmentation, not replacement. Engineers remain fully in control. Agents surface recommendations, automate calculations, flag risks, and generate reports — but every critical design decision is reviewed, validated, and owned by the engineer. The system supports judgment, it does not replace it.
    Domain-Aware — Generic AI is not sufficient for engineering work. Each agent is grounded in domain-specific knowledge — suspension dynamics, DFMEA methodology, V&V standards, load cases — not just language understanding. The intelligence is engineering-first, not generic-first.
    Extensible — The agent layer is not fixed. As needs evolve, new agents can be added to any subsystem — cost estimation, supplier selection, regulatory compliance, weight optimization. The architecture is built to accommodate this without structural change.
Notes: 1.7.2013
2
‹#›

## Slide 5
PR
Ride Optimization
Madhupranavi S
Physics-based and surrogate modelling approaches for suspension stiffness and damping optimisation
Notes: 1.7.2013
1
‹#›

## Slide 6
Goal:
Determine optimal suspension parameters for a 6×2 vehicle with Non-Reactive Suspension (NRS) to minimize cabin seat RMS acceleration.
Develop a fast and accurate suspension dynamics model that captures full system behavior and supports efficient optimization to automatically identify the optimal stiffness and damping configuration for improved ride comfort.
The suspension system is a key component influencing ride comfort and driving performance.
  Heavy commercial vehicles experience continuous road excitations, transmitting vibrations through the suspension to the cabin and ultimately the driver seat.
  Ride comfort is quantified using RMS acceleration at the cabin seat, a standard measure of whole-body vibration linked to: Driver fatigue, Discomfort, Long-term health impacts
Ride Optimisation
Notes: 1.7.2013
11
‹#›

## Slide 7
The rear tandem axles are mechanically coupled, which is a defining feature of the NRS setup. This arrangement allows load sharing without inducing additional pitch or roll moments, helping maintain vehicle attitude stability
System Definition
The system under consideration is a 6×2 heavy commercial vehicle equipped with a Non-Reactive Suspension (NRS) configuration, designed to improve ride comfort and stability.
  Consists of the cabin and chassis (sprung mass) with bounce (z), pitch (θ), and roll (ϕ) motions.
  Each of the three axles exhibits bounce (z) and roll (ϕ) dynamics.
Notes: 1.7.2013
11
‹#›

## Slide 8
System Definition
The system is formulated using axle displacements, with primary focus on cabin seat-level RMS acceleration.
Minimize cabin seat-level RMS acceleration through parameter optimization.
Tunable Parameters
  KF – Front axle spring stiffness
  CF – Front axle damping
  K2 – Rear axle 1 spring stiffness
  K3 – Rear axle 2 spring stiffness
Notes: 1.7.2013
11
‹#›

## Slide 9
Two Approaches
Physics-Based Approach
WORKFLOW
1. Define Suspension ODE System
↓
2. Simulate Road Input → ODE Solve
↓
3. Extract RMS Acceleration
↓
4. Optimise Stiffness & Damping
✓ Physically reliable — grounded in mechanics
✓ No training data required
✓ Interpretable and explainable results
✗ Computationally expensive — 10–11 hrs per run
✗ Every parameter change requires full re-run
Deep Learning Surrogate Approach
WORKFLOW
1. Generate training data from ODE simulations
↓
2. Train deep learning model on system response
↓
3. Trained model predicts RMS in milliseconds
↓
4. Plug into optimiser — repeated runs at low cost
✓ Near-instant inference once trained
✓ Scales easily — no re-simulation needed
✓ Real measurement data can be incorporated
✗ Upfront cost — data generation and training
✗ Accuracy bounded by training data quality
Notes: 1.7.2013
11
‹#›

## Slide 10
The physics-based approach involves solving the ODEs (as mentioned earlier), which are detailed here and these equations describe the system dynamics and are used to obtain the response.
Physics Based Approach
Notes: 1.7.2013
11
‹#›

## Slide 11
The ODEs mentioned above are represented as 6-DOF suspension model with two geometric constraints:
Now, formulating the constrained KKT conditions based on the above: to enforce the constraints, introduce Lagrange multipliers λ, which generate constraint forces, where G(q)=∂g/∂q.
Physics Based Approach
Baumgarte stabilization corrects this drift continuously by adding a term, which behaves like a critically damped spring pulling the constraint back toward zero.
And it has a damping ratio and a correction stiffness that control how fast the constraint error is removed.
This is solved using the standard KKT formulation with
Notes: 1.7.2013
11
‹#›

## Slide 12
Design Approaches for Two-Stage Asymmetric Damper Integration:
Option 1: Direct Optimization – Two-Stage Asymmetric Damper
  The nonlinear damper characteristics are optimized directly, along with key vehicle and suspension stiffness parameters.
  Optimization is performed using the fully nonlinear damping model within the ODE framework.
  The optimization simultaneously tunes:
  1. K_F , C_F , K_2 , K_3
  2. Damping parameters: cs− , Asymmetry Ratio, γc , γr
  Option 2: Two-Phase Optimization with Curve Fitting
  A two-phase strategy is adopted to improve robustness and reduce computational complexity:
  Phase 1: Linear Optimization
  Optimize linear suspension and damper parameters: K_F , C_F , K_2 , K_3
  Phase 2: Nonlinear Curve Fitting
  Fit nonlinear damper parameters based on optimized linear response: cs− , Asymmetry Ratio, γc , γr
  The front damper relative velocity time history from Phase 1 represents the actual operating velocity distribution.
  Nonlinear damper parameters are identified using a weighted least-squares curve fitting approach.
Shock Absorbing Character
Notes: 1.7.2013
11
‹#›

## Slide 13
Shock Absorbing Character
Results and Observation:
Notes: 1.7.2013
11
‹#›

## Slide 14
Shock Absorbing Character
Both approaches — directly optimising with the nonlinear damper embedded in the ODE and optimising for linear parameters followed by a curve fit — produced comparable RMS acceleration results. Since the performance is equivalent, Option 1 is the preferred approach. Embedding the nonlinear damper directly into the optimisation ensures the solver always operates on the true system representation, eliminating the post-processing curve fitting step, preserving physical consistency throughout, and reducing the risk of approximation error introduced by fitting a nonlinear curve after the fact. This makes Option 1 the cleaner and more rigorous pipeline.
Observation:
Notes: 1.7.2013
11
‹#›

## Slide 15
Optimisation
The design approach considers: Single-objective optimization & Multi-objective optimization
The cabin seat RMS (Root Mean Square) is computed based on: Bounce acceleration (ẍc), Roll acceleration (ϕ̈c), Pitch acceleration (θ̈c)
These accelerations are evaluated at the seat level to assess ride comfort.
Optimization can be applied as:
  Single-objective optimization → Focus on minimizing a scalar objective function, aggregate effect of multiple DOFs
  Multi-objective optimization → Optimize each DOF independently to obtain trade-off solutions
Notes: 1.7.2013
11
‹#›

## Slide 16
Results & Observation
Notes: 1.7.2013
11
‹#›

## Slide 17
The Plots corresponding to
Results & Observation
Notes: 1.7.2013
11
‹#›

## Slide 18
The Plots corresponding to
Results & Observation
Notes: 1.7.2013
11
‹#›

## Slide 19
Key Observation:
Multi-objective optimisation (NSGA-II) outperforms single-objective — it captures the full trade-off space and gives the engineer flexibility to select a solution based on priority. Both methods are available and the choice can be embedded in the workflow based on design parameters and the frequency range of interest.
The Bottleneck:
The physics-based approach, despite its reliability, takes an average of 10–11 hours per full optimisation run. Any change to the setup — road class, speed, parameter bounds, damper model — requires a complete re-run. For a team iterating rapidly across design variants, this is a significant bottleneck.
Inference and Transition
Why Physics-Based Remains Valuable
→ Ground truth — results are exact by construction
→ No data dependency — works from first principles
→ Essential for validation of any surrogate model
→ Full interpretability of optimised parameters
Why a Surrogate Model Makes Sense
→ Once trained — full optimisation in minutes
→ Repeated design iterations at negligible compute cost
→ Real measurement data can be fed into training directly
→ Scales across configurations without re-simulation
To get the speed advantage of a surrogate while preserving physical reliability, we build a Physics-Informed Neural Network — a deep learning model trained not just on simulation data but constrained by the governing equations of motion. The network can only learn solutions that are physically consistent.
Notes: 1.7.2013
11
‹#›

## Slide 20
Surrogate Modelling
What PINN does differently
A Physics-Informed Neural Network embeds the governing ODE directly into the training loss. The network is penalised not just for deviating from data but also for violating the physics of the system — forcing it to learn solutions that are physically consistent even where data is sparse.
Data Loss: Ldata​=MSE(y^​,y) Physics Loss: Lphys​=(ODE Residual)2
Total Loss: L=λ1Ldata+λ2Lphys
Detailed picture of Architecture diagram:
Notes: 1.7.2013
11
‹#›

## Slide 21
Surrogate Modelling
Detailed Architecture:
Road Inputs + Physical Parameters → TCN Encoder + Parameter MLP → Feature Fusion → LSTM → State & Acceleration Heads → Physics-Informed Loss
Training evaluvation:
Notes: 1.7.2013
11
‹#›

## Slide 22
Test Evaluvation:
Surrogate Modelling
The surrogate modelling approach, trained on the current simulation dataset, successfully converged to an optimised solution with a cabin seat RMS acceleration of ______ m/s². This demonstrates that the trained model has sufficiently captured the suspension system dynamics to drive meaningful optimisation. The framework is deployment-ready — substituting the simulation dataset with real measured road and vehicle response data would further improve prediction accuracy and make the optimised parameters directly reflective of real operating conditions.
Notes: 1.7.2013
11
‹#›

## Slide 23
Generalised Framework
Framework Highlights
  Integrates both surrogate-based and ODE-based approaches, making the framework highly adaptable and flexible.
  Enables seamless switching between different use cases and modeling strategies.
  Supports a wide range of optimization algorithms for diverse problem requirements.
  Facilitates effective comparison of results to support better decision-making.
Notes: 1.7.2013
11
‹#›

## Slide 24
Fitting in Agentic Architecture
The ODE, solver, and optimiser are tools the agent calls — they do not decide whether results make sense or what to do when something goes wrong. That is the agent's job.
At every stage, the agent chooses one of four paths:
Proceed — stage completed cleanly, move forward. Retry — recoverable failure, reattempt before deciding whether to continue. Warn — completed but result is outside expected bounds, flag it and continue. Stop — failure makes continuing meaningless, halt and return a structured explanation.
Every decision is recorded — which path, and why. That audit trail is part of the structured output available to downstream agents and the user.
The physics never changes run to run. What the agent adds is the reasoning layer above it — deciding whether the tools are working, whether results are trustworthy, and ensuring nothing downstream receives incomplete information.
1
Parse &
Validate
Physics code checked for syntax & model validity
2
Load
Road Data
Input road profile loaded & verified
3
Pre-flight
Test
Stability check; compute-time estimate
4
Run
Optimiser
Multi-objective (Pareto) or single-objective
5
Generate
Outputs
Results packaged into structured summary
Notes: 1.7.2013
11
‹#›

## Slide 25
Demo
Notes: 1.7.2013
11
‹#›

## Slide 26
Thank You!
Questions?
Let's dig in.
Notes: 1.7.2013
11
‹#›